ATAL COMMUNITY DAY
HANDOUT
Online repository for the content
github.com/adiagr/atl

Breadboard connections

Circuit Diagrams

Normal LED	Parallel LED	Series LED	LED with Switch

Relay

Common Sensors

Sensor Name	Means of operation	Uses
HCSR-04 Ultrasonic Sensor	Ultrasonic waves	Finding distance
IR sensor	Infrared Light	Distance, Gesture, Color
Light Dependent resistance	Visible Light	Color, ambient light intensity
DHT-11 Temprature humidity	Temprature and moisture	To measure temprature, humidity
MQ-2 Smoke Sensor	Coil	Detect Smoke, LPG, etc

Arduino Cheat Sheet
Remember!!

First set the input mode of the pin
USE:
pinMode(pinNumber, Mode[INPUT/OUTPUT])

Arduino is Case-Sensitive

void setup() executes only once before void loop(), do all your initializing in void setup()

Put your main code in void loop()
that will loop over and over

Output Functions:

digitalWrite(PinNumber, Mode[HIGH/LOW])

analogWrite(PinNumber, Value[0-255])

Input Functions

digitalRead(pinNumber)

analogRead(pinNumber)

pulseIn(pinNumber, type[HIGH/LOW])

Time

delay(Time-in-milliseconds)

delayMicroseconds(Time-in-microseconds)

Serial Functions

Serial.begin(Baud-Rate[9600])

Serial.println(“Message”) //This prints a new line

Serial.print(“This outputs in the same line”)